## Slide 1
AXI4 RTL Verification Project
AXI-Lite Register File · AXI4 Memory Model · Simple AXI4 Master
Vivado / xsim · SystemVerilog Testbenches · Automated CI Gate
3
RTL / Model Components
177
Total Checks Passed
0
Failures
3
CI Gate Scripts
Bumhee Lee · 2026-05-01

## Slide 2
Project Architecture Overview

## Slide 3
AXI-Lite Register File (rtl/axi_lite_regfile.v)
4 × 32-bit regs | Byte-WSTRB | 3 write paths (W_IDLE/W_WAIT_W/W_WAIT_A) | SLVERR for addr[31:4]≠0 | 133/133 checks passed

## Slide 4
AXI-Lite Register File — Verification Coverage (133 Checks)
133 / 133 checks PASSED · 0 failures · CI exit code 0 · Simulation time 3720 ns

## Slide 5
AXI4 Memory Model (tb/axi_mem_model.sv)
Parameterised MEM_DEPTH / MEM_BASE · 30/30 checks PASSED · Simulation time 690 ns

## Slide 6
Simple AXI4 Master — 6-State FSM (rtl/simple_axi_master.v)
Combinatorial AXI outputs from FSM state · Registered data latches · done pulses for exactly one cycle

## Slide 7
Simple AXI4 Master — Transaction Timing & Test Results
14/14 checks PASSED · CI exit code 0 · Simulation time 445 ns

## Slide 8
Summary & Overall Verification Status
AXI-Lite Register File
rtl/axi_lite_regfile.v
133 / 133
checks
▸ 4 × 32-bit registers
▸ SLVERR on addr[31:4]≠0
▸ 3 write FSM paths
▸ Backpressure coverage
AXI4 Memory Model
tb/axi_mem_model.sv
30 / 30
checks
▸ 1 KB parameterised RAM
▸ Byte-WSTRB do_write()
▸ SLVERR for OOB addresses
▸ Initial zero guarantee
Simple AXI4 Master
rtl/simple_axi_master.v
14 / 14
checks
▸ 6-state FSM
▸ Write → Readback sequence
▸ Error flag: SLVERR / mismatch
▸ Comb. AXI output drivers
Total: 177 / 177 checks passed · 0 failures · 3 CI scripts · All exit code 0